## Slide 1
Background and Introduction
Mustafa Ozdal

## Slide 2: Chapter 1 – Introduction
Original Authors:
Andrew B. Kahng, Jens Lienig, Igor L. Markov, Jin Hu
VLSI Physical Design: From Graph Partitioning to Timing Closure
SOME SLIDES ARE FROM THE BOOK:
MODIFICATIONS WERE MADE ON THE ORIGINAL SLIDES

## Slide 3: 1.1 Electronic Design Automation (EDA)
Moore’s Law
In 1965, Gordon Moore (Fairchild) stated that the number of transistors on an IC would double every year. 10 years later, he revised his statement, asserting that they double every 18 months. Since then, this “rule” has been famously known as Moore’s Law.
Moore: „Cramming more components onto integrated circuits"
Electronics, Vol. 38, No. 8, 1965

## Slide 4: 1.1 Electronic Design Automation (EDA)
Without the design technology innovations between 1993 and 2007, the design cost of a chip would have been $1800M

## Slide 5: 1.1 Electronic Design Automation (EDA)
Design for Manufacturability (DFM), optical proximity correction (OPC), and other techniques emerge at the design-manufacturing interface. Increased reusability of blocks, including intellectual property (IP) blocks.
2000 - now
First over-the-cell routing, first 3D and multilayer placement and routing techniques developed. Automated circuit synthesis and routability-oriented design become dominant. Start of parallelizing workloads. Emergence of physical synthesis.
1990 -2000
First performance-driven tools and parallel optimization algorithms for layout; better understanding of underlying theory (graph theory, solution complexity, etc.).
1985 -1990
More advanced tools for ICs and PCBs, with more sophisticated algorithms.
1975 -1985
Layout editors, e.g., place and route tools, first developed for printed circuit boards.
1965 -1975
Manual design only.
1950 -1965
Circuit and Physical Design Process Advancements
Time Period
© 2011 Springer Verlag

## Slide 6: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
© 2011 Springer Verlag
Goals and requirements:
Functionality, performance, dimensions, etc.

## Slide 7: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
© 2011 Springer Verlag
e.g. Instruction set, memory
system, number of cores,
communication protocols, …

## Slide 8: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
© 2011 Springer Verlag
Hardware description using
RTL. Logic synthesis tools to
generate netlists.

## Slide 9: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
© 2011 Springer Verlag
Transistor-level design of
low level elements, e.g.
SRAMs, IO, critical blocks,…

## Slide 10: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis
© 2011 Springer Verlag

## Slide 11: Physical Design
A
C
B
D
E
F
Netlist
Logic gates & connections
Shapes on chip layers
Chip Layers
Device layers
Metal layers

## Slide 12: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
© 2011 Springer Verlag
Design rule checking (DRC)
Layout vs. schematic (LVS)
Electrical rule checking (ERC)

## Slide 13: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
© 2011 Springer Verlag
Layout sent to a fab (tapeout).
Photomasks used to print the layout patterns onto layers.

## Slide 14: 1.2 VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
© 2011 Springer Verlag
Die is positioned in a package. Pins connected to the package pins. Multiple chips can be integrated.

## Slide 15: VLSI Design Styles
Full-custom design
  Direct transistor-level design
  Max flexibility, few constraints
  Potential to highly optimize, but high design cost
  Critical and high-volume parts that will be replicated
Semi-custom design
  Cell-based: Standard and macro cells
    Many pre-designed elements in the libraries
  Array-based: Configure the pre-fabricated elements
    e.g. FPGA

## Slide 16: Cell Based Design
Common digital cells
 | IN | OUT
 | 0 | 1
 | 1 | 0
 | 1 | 0
 | 1 | 1
OR
INV
NOR
NAND
AND
IN1 | IN2 | OUT
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
IN1 | IN2 | OUT
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
IN1 | IN2 | OUT
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
IN1 | IN2 | OUT
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 17: 1.3 VLSI Design Styles
Vdd
GND
OUT
IN2
IN1
OUT
IN2
IN1
OUT
IN1
Vdd
GND
IN2
Contact
Diffusion layer
p-type transistor
n-type transistor
Metal layer
Poly layer

## Slide 18: 1.3 VLSI Design Styles
Power (Vdd)-Rail
Ground (GND)-Rail
Contact
Vdd
GND
OUT
IN2
IN1
OUT
IN2
IN1
OUT
IN1
Vdd
GND
IN2
Diffusion layer
p-type transistor
n-type transistor
Metal layer
Poly layer

## Slide 19: Cell Placement
A
C
B
D
E
F
Metal 1
Device layers
Implementation on device layers available in cell library
(e.g. AND, OR, NAND, NOR, INV, etc.)
Cells arranged in rows on metal1

## Slide 20: 1.3 VLSI Design Styles
Standard cell layout with a feedthrough cell
A
GND
Feedthrough Cell
Pad
Ground Pad
Routing Channel
Standard Cells
Power Pad
GND
Pad
Ground Pad
Standard Cells
Power Pad
A’
A
A’
VDD
VDD
Standard cell layout using over-the-cell (OTC routing
© 2011 Springer Verlag

## Slide 21: Over-the-cell routing
A
C
B
D
E
F
All terminals on metal1
Connect terminals using metal layers
Each layer is either horizontal or vertical
a
b
o
a
a
a
o
o
o
a
b
a
o
o
b
Metal1
Metal2
Metal3
Metal4
Metal5

## Slide 22: Routing Between Two Pins
Route from C/o to D/a
Metal3: vertical
Metal2: horizontal
Metal1: escape-only
Interlayer connection: “via”
Metal1
o
a
b
C
o
a
D
Metal2
Metal3
C
D
a
b
o
a
o

## Slide 23: Cell Based Design
Layout with macro cells
Pad
GND
PLA
RAM
Standard Cell Block
RAM
PLA
Routing Regions
VDD
© 2011 Springer Verlag

## Slide 24: Why Cell Based Design?
Easier to design, optimize and verify
  Reuse of components
  Performance of each cell pre-characterized
  Transistor-level design constraints already handled
  Complexities abstracted in the cell definition
  Optimization easier
Disadvantage: Less room for optimization
  Cannot have a cell for every single complex logic function

## Slide 25: Field Programmable Gate Array (FPGA)
LB
LB
LB
SB
SB
LB
LB
LB
SB
SB
LB
LB
LB
LB
LB
LB
SB
SB
LB
LB
LB
SB
SB
LB
LB
LB
LB
LB
SB
SB
LB
LB
LB
SB
SB
LB
LB
LB
Logic Element
Switchbox
LB
Connection
© 2011 Springer Verlag
After fabrication:
Each logic element can be configured to implement different functions
Each switchbox can be configured to change the connectivity

## Slide 26: 1.4. Design Rules
Size rules, such as minimum width: The dimensions of any component (shape), e.g., length of a boundary edge or area of the shape, cannot be smaller than given minimum values. These values vary across different metal layers.
Separation rules, such as minimum separation: Two shapes, either on the same layer or on adjacent layers, must be a minimum (rectilinear or Euclidean diagonal) distance apart.
Overlap rules, such as minimum overlap: Two connected shapes on adjacent layers must have a certain amount of overlap due to inaccuracy of mask alignment to previously-made patterns on the wafer.
Categories of design rules

## Slide 27: 1.4. Design Rules
Categories of design rules
Minimum Width: a Minimum Separation: b, c, d
Minimum Overlap: e
a
d
c

b
e
: smallest meaningful technology-dependent unit of length
© 2011 Springer Verlag

## Slide 28: 1.5 Physical Design Optimizations
Technology constraints enable fabrication for a specific technology node and are derived from technology restrictions. Examples include minimum layout widths and spacing values between layout shapes.
Electrical constraints ensure the desired electrical behavior of the design. Examples include meeting maximum timing constraints for signal delay and staying below maximum coupling capacitances.
Geometry (design methodology) constraints are introduced to reduce the overall complexity of the design process. Examples include the use of preferred wiring directions during routing, and the placement of standard cells in rows.
Types of constraints

## Slide 29: 1.6 Algorithms and Complexity
Runtime complexity: the time required by the algorithm to complete as a function of some natural measure of the problem size, allows comparing the scalability of various algorithms
Complexity is represented in an asymptotic sense, with respect to the input size n, using big-Oh notation or O(…)
Runtime t(n) is order f (n), written as t(n) = O(f (n))
where k is a real number
Example: t(n) = 7n! + n2 + 100, then t(n) = O(n!) because n! is the fastest growing term as n  .
Runtime complexity

## Slide 30: 1.6 Algorithms and Complexity
Example: Exhaustively Enumerating All Placement Possibilities
  Given: n cells
  Task: find a single-row placement of n cells with minimum total wirelength by using exhaustive enumeration.
  Solution: The solution space consists of n! placement options. If generating and evaluating the wirelength of each possible placement solution takes 1 s and n = 20, the total time needed to find an optimal solution would be 77,147 years!
A number of physical design problems have best-known algorithm complexities that grow exponentially with n, e.g., O(n!), O(nn), and O(2n).
Many of these problems are NP-hard (NP: non-deterministic polynomial time)
  No known algorithms can ensure, in a time-efficient manner, globally optimal solution
Heuristic algorithms are used to find near-optimal solutions
Runtime complexity

## Slide 31: 1.6 Algorithms and Complexity
Deterministic: All decisions made by the algorithm are repeatable, i.e., not random. One example of a deterministic heuristic is A* shortest path algorithm.
Stochastic: Some decisions made by the algorithm are made randomly, e.g., using a pseudo-random number generator. Thus, two independent runs of the algorithm will produce two different solutions with high probability. One example of a stochastic algorithm is simulated annealing.
In terms of structure, a heuristic algorithm can be
  Constructive: The heuristic starts with an initial, incomplete (partial) solution and adds components until a complete solution is obtained.
  Iterative: The heuristic starts with a complete solution and repeatedly improves the current solution until a preset termination criterion is reached.
Heuristic algorithms

## Slide 32: 1.6 Algorithms and Complexity
Heuristic algorithms
Constructive Algorithm
Iterative Improvement
no
yes
Termination Criterion Met?
Return Best-Seen Solution
Problem Instance
Initial Solution

## Slide 33: 1.7 Graph Theory Terminology
Graph
Hypergraph
Multigraph
a
b
c
d
e
f
g
b
e
d
a
c
f
a
b
c
© 2011 Springer Verlag

## Slide 34: 1.7 Graph Theory Terminology
Directed graphs with cycles
Directed acyclic graph
c
a
b
d
e
f
g
a
b
c
a
b
d
e
f
g
© 2011 Springer Verlag

## Slide 35: 1.7 Graph Theory Terminology
Undirected graph with maximum node degree 3
Directed tree
a
b
c
d
e
f
g
a
b
c
d
e
f
g
h
i
j
k
© 2011 Springer Verlag

## Slide 36: 1.7 Graph Theory Terminology
Rectilinear minimum spanning tree (RMST)
Rectilinear Steiner minimum tree (RSMT)
b (2,6)
a (2,1)
c (6,4)
c (6,4)
Steiner point
b (2,6)
a (2,1)
© 2011 Springer Verlag

## Slide 37: 1.8 Common EDA Terminology
Netlist
a
b
x
y
z
c
N1
N2
N3
N4
(a: N1)
(b: N2)
(c: N5)
(x: IN1 N1, IN2 N2, OUT N3)
(y: IN1 N1, IN2 N2, OUT N4)
(z: IN1 N3, IN2 N4, OUT N5)
(N1: a, x.IN1, y.IN1)
(N2: b, x.IN2, y.IN2)
(N3: x.OUT, z.IN1)
(N4: y.OUT, z.IN2)
(N5: z.OUT, c)
Pin-Oriented Netlist
Net-Oriented Netlist
N5
© 2011 Springer

## Slide 38: 1.8 Common EDA Terminology
Connectivity graph
a
b
x
y
z
c
N1
N2
N3
N4
N5
a
b
x
y
z
c
© 2011 Springer Verlag

## Slide 39: 1.8 Common EDA Terminology
Connectivity matrix
a
b
x
y
z
c
N1
N2
N3
N4
N5
0
1
0
0
0
0
c
1
0
1
1
0
0
z
0
1
0
2
1
1
y
0
1
2
0
1
1
x
0
0
1
1
0
0
b
0
0
1
1
0
0
a
c
z
y
x
b
a
© 2011 Springer Verlag

## Slide 40: 1.8 Common EDA Terminology
Distance metric between two points P1 (x1,y1) and P2 (x2,y2)
P1 (2,4)
P2 (6,1)
dM = 7
dM = 7
with n = 2: Euclidean distance
n = 1: Manhattan distance
dE = 5

## Slide 41: Next Lecture: Netlist and System Partitioning
2.1 Introduction
2.2 Terminology
2.3 Optimization Goals
2.4 Partitioning Algorithms
  2.4.1 Kernighan-Lin (KL) Algorithm
  2.4.2 Extensions of the Kernighan-Lin Algorithm
  2.4.3 Fiduccia-Mattheyses (FM) Algorithm
2.5 Framework for Multilevel Partitioning
  2.5.1 Clustering
  2.5.2 Multilevel Partitioning
2.6 System Partitioning onto Multiple FPGAs