## Slide 1
Partitioning
Mustafa Ozdal

## Slide 2: Chapter 2 – Netlist and System Partitioning
Original Authors:
Andrew B. Kahng, Jens Lienig, Igor L. Markov, Jin Hu
VLSI Physical Design: From Graph Partitioning to Timing Closure
MOST SLIDES ARE FROM THE BOOK:
MODIFICATIONS WERE MADE ON THE ORIGINAL SLIDES

## Slide 3: Chapter 2 – Netlist and System Partitioning
2.1 Introduction
2.2 Terminology
2.3 Optimization Goals
2.4 Partitioning Algorithms
  2.4.1 Kernighan-Lin (KL) Algorithm
  2.4.2 Extensions of the Kernighan-Lin Algorithm
  2.4.3 Fiduccia-Mattheyses (FM) Algorithm
2.5 Framework for Multilevel Partitioning
  2.5.1 Clustering
  2.5.2 Multilevel Partitioning
2.6 System Partitioning onto Multiple FPGAs

## Slide 4: 2.1 Introduction
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis

## Slide 5: Divide and Conquer Strategy for Chip Design
Partition the design. Then, work on each partition separately
Advantages:
  Parallel implementation of each part by different designers
  Tool capacity issues avoided
Disadvantages:
  Potentially less room for optimization
  Inter-dependency between different partitions
  Difficulty of combining partitions at the end

## Slide 6: 2.1 Introduction
Circuit:
Cut ca: four external connections
1
2
4
5
3
6
7
8
5
6
4
8
7
2
3
1
5
6
4
8
7
2
3
1
Cut ca
Cut cb
Block A
Block B
Block A
Block B
Cut cb: two external connections

## Slide 7: 2.2 Terminology
5
6
4
2
1
3
3
2
4
5
6
1
Graph G2: Nodes 1, 2, 6.
Graph G1: Nodes 3, 4, 5.
Collection of cut edges Cut set: (1,3), (2,3), (5,6),
Block (Partition)
Cells
cut edge: connects nodes in different partitions

## Slide 8: 2.3 Optimization Goals
Given a graph G(V,E) with |V| nodes and |E| edges where each node v  V and each edge e  E.
Each node has area s(v) and each edge has cost or weight w(e).
The objective is to divide the graph G into k disjoint subgraphs such that all optimization goals are achieved:
  Number (or total weight) of connections between partitions is minimized
  Partition sizes are balanced
NP-hard problem
Efficient heuristics are developed in the 1970s and 1980s. They are high quality and in low-order polynomial time.

## Slide 9: Chapter 2 – Netlist and System Partitioning
2.1 Introduction
2.2 Terminology
2.3 Optimization Goals
2.4 Partitioning Algorithms
  2.4.1 Kernighan-Lin (KL) Algorithm
  2.4.2 Extensions of the Kernighan-Lin Algorithm
  2.4.3 Fiduccia-Mattheyses (FM) Algorithm
2.5 Framework for Multilevel Partitioning
  2.5.1 Clustering
  2.5.2 Multilevel Partitioning
2.6 System Partitioning onto Multiple FPGAs

## Slide 10: 2.4.1 Kernighan-Lin (KL) Algorithm
Given: A graph with 2n nodes where each node has the same weight.
Goal: A partition (division) of the graph into two disjoint subsets A and B with minimum cut cost and |A| = |B| = n.
2
5
6
3
1
4
7
8
Example: n = 4
Block A
Block B

## Slide 11: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain D(v) of a node v
D(v) = |Ec(v)| – |Enc(v)| ,
where
Ec(v) is the set of v’s incident edges that are cut by the cut line, and
Enc(v) is the set of v’s incident edges that are not cut by the cut line.
High gains (D > 0) indicate that the node should move, while low gains (D < 0) indicate that the node should stay within the same partition.
2
5
6
3
1
4
7
8
Node 3:
D(3) = 3-1=2
Node 7:
D(7) = 2-1=1

## Slide 12: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain of swapping a pair of nodes a and b
g = D(a) + D(b) - 2* c(a,b),
where
D(a), D(b) are the respective gains of nodes a, b
c(a,b) is the connection weight between a and b:
If an edge exists between a and b, then c(a,b) = edge weight (here 1),
otherwise, c(a,b) = 0.
The gain g indicates how useful the swap between two nodes will be
The larger g, the more the total cut cost will be reduced
2
5
6
3
1
4
7
8

## Slide 13: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain of swapping a pair of nodes a und b
g = D(a) + D(b) - 2* c(a,b),
where
D(a), D(b) are the respective gains of nodes a, b
c(a,b) is the connection weight between a and b:
If an edge exists between a and b, then c(a,b) = edge weight (here 1),
otherwise, c(a,b) = 0.
2
5
6
3
1
4
7
8
Node 3:
D(3) = 3-1=2
Node 7:
D(7) = 2-1=1
g (3,7) = D(3) + D(7) - 2* c(a,b) = 2 + 1 – 2 = 1
=> Swapping nodes 3 and 7 would reduce the cut size by 1
2
5
6
3
1
4
7
8

## Slide 14: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain of swapping a pair of nodes a und b
g = D(a) + D(b) - 2* c(a,b),
where
D(a), D(b) are the respective gains of nodes a, b
c(a,b) is the connection weight between a and b:
If an edge exists between a and b, then c(a,b) = edge weight (here 1),
otherwise, c(a,b) = 0.
2
5
6
3
1
4
7
8
Node 3:
D(3) = 3-1=2
Node 5:
D(5) = 2-1=1
g (3,5) = D(3) + D(5) - 2* c(a,b) = 2 + 1 – 0 = 3
=> Swapping nodes 3 and 5 would reduce the cut size by 3
2
5
6
3
1
4
7
8

## Slide 15: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Gain of swapping a pair of nodes a and b
The goal is to find a pair of nodes a and b to exchange such that g is maximized and swap them.

## Slide 16: 2.4.1 Kernighan-Lin (KL) Algorithm – Terminology
Maximum positive gain Gm of a pass
The maximum positive gain Gm corresponds to the best prefix of m swaps within the swap sequence of a given pass.
These m swaps lead to the partition with the minimum cut cost encountered during the pass.
Gm is computed as the sum of Δg values over the first m swaps of the pass, with m chosen such that Gm is maximized.

## Slide 17: 2.4.1 Kernighan-Lin (KL) Algorithm

## Slide 18: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
2
5
6
3
1
4
7
8
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8

## Slide 19: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
2
5
6
3
1
4
7
8
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1
gains D(v) of each node:
Nodes that lead to maximum gain

## Slide 20: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
2
5
6
3
1
4
7
8
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
Nodes that lead to maximum gain
Gain in the current pass
gains D(v) of each node:
Gain after node swapping

## Slide 21: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
2
5
6
3
1
4
7
8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
Nodes that lead to maximum gain
Gain in the current pass
Gain after node swapping
2
5
6
3
1
4
7
8

## Slide 22: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
Cut cost: 6
Not fixed: 1,2,4,6,7,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 23: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
Cut cost: 6
Not fixed: 1,2,4,6,7,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 24: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
Cut cost: 6
Not fixed: 1,2,4,6,7,8
2
5
6
3
1
4
7
8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
Nodes that lead to maximum gain
Gain in the current pass
Gain after node swapping
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 25: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
Cut cost: 6
Not fixed: 1,2,4,6,7,8
Cut cost: 1
Not fixed: 1,2,7,8
2
5
6
3
1
4
7
8
Cut cost: 7
Not fixed: 2,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
Gain in the current pass
Nodes that lead to maximum gain
Gain after node swapping
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 26: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Cut cost: 9
Not fixed: 1,2,3,4,5,6,7,8
2
5
6
3
1
4
7
8
Cut cost: 9
Not fixed: –
Cut cost: 6
Not fixed: 1,2,4,6,7,8
Cut cost: 1
Not fixed: 1,2,7,8
Cut cost: 7
Not fixed: 2,8
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
D(2) = -1 D(8)=-1
g4 = -1-1-0 = -2
Swap (2,8)
G4 = G3 +g4 = 0
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8
2
5
6
3
1
4
7
8

## Slide 27: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
Maximum positive gain Gm = 8 with m = 2.
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
D(2) = -1 D(8)=-1
g4 = -1-1-0 = -2
Swap (2,8)
G4 = G3 +g4 = 0

## Slide 28: 2.4.1 Kernighan-Lin (KL) Algorithm – Example
D(1) = 1 D(5) = 1 D(2) = 1 D(6) = 2 D(3) = 2 D(7) = 1 D(4) = 1 D(8) = 1 g1 = 2+1-0 = 3
Swap (3,5)
G1 = g1 =3
D(1) = -1 D(6) = 2 D(2) = -1 D(7)=-1 D(4) = 3 D(8)=-1 g2 = 3+2-0 = 5
Swap (4,6)
G2 = G1+g2 =8
D(1) = -3 D(7)=-3 D(2) = -3 D(8)=-3 g3 = -3-3-0 = -6
Swap (1,7)
G3= G2 +g3 = 2
D(2) = -1 D(8)=-1
g4 = -1-1-0 = -2
Swap (2,8)
G4 = G3 +g4 = 0
Since Gm > 0, the first m = 2 swaps (3,5) and (4,6) are executed.
2
5
6
3
1
4
7
8
Since Gm > 0, more passes are needed until Gm  0.
Maximum positive gain Gm = 8 with m = 2.

## Slide 29: 2.4.1 Kernighan-Lin (KL) Algorithm – Complexity Analysis
1-pass runtime: O(n3)
Optimized implementation: O(n2lgn)
O(n)
O(n2)
O(n2)
O(n)
O(n)
n times
n: # of nodes in each partition

## Slide 30: 2.4.2 Extensions for Kernighan-Lin (KL) Algorithm
Unequal partition sizes
Unequal cell sizes or unequal node weights
k-way partitioning (generating k partitions)
30

## Slide 31: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm
Single cells are moved independently instead of swapping pairs of cells. Thus, this algorithm is applicable to partitions of unequal size or the presence of initially fixed cells.
Cut costs are extended to include hypergraphs, i.e., nets with two or more pins. While the KL algorithm aims to minimize cut costs based on edges, the FM algorithm minimizes cut costs based on nets.
The area of each individual cell is taken into account.
Nodes and subgraphs are referred to as cells and blocks, respectively.

## Slide 32: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm
Given: a graph G(V,E) with nodes and weighted edges
Goal: to assign all nodes to disjoint partitions, so as to minimize the total cost (weight) of all cut nets while satisfying partition size constraints

## Slide 33: Fiduccia-Mattheyses (FM) Algorithm – Terminology
FS(c): the # of cut nets connected only to cell c in c’s partition
“moving force”
c
FS(c) = 1

## Slide 34: Fiduccia-Mattheyses (FM) Algorithm – Terminology
TE(c): the # of uncut nets connected to cell c
“retention force”
c
TE(c) = 1

## Slide 35: Fiduccia-Mattheyses (FM) Algorithm – Terminology
Δg(c) = FS(c) – TE(c)
“gain of moving c”
c
Δg(c) = 0

## Slide 36: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Gain g(c) for cell c
g(c) = FS(c) – TE(c) ,
where
the “moving force“ FS(c) is the number of nets connected to c but not connected to any other cells within c’s partition, i.e., cut nets that connect only to c, and
the “retention force“ TE(c) is the number of uncut nets connected to c.
The higher the gain g(c), the higher is the priority to move the cell c to the other partition.
Cell 2: FS(2) = 0 TE(2) = 1 g(2) = -1
1
3
4
2
5
a
b
c
d
e

## Slide 37: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Gain g(c) for cell c
g(c) = FS(c) – TE(c) ,
where
the “moving force“ FS(c) is the number of nets connected to c but not connected to any other cells within c’s partition, i.e., cut nets that connect only to c, and
the “retention force“ TE(c) is the number of uncut nets connected to c.
Cell 1: FS(1) = 2 TE(1) = 1 g(1) = 1
Cell 2: FS(2) = 0 TE(2) = 1 g(2) = -1
Cell 3: FS(3) = 1 TE(3) = 1 g(3) = 0
Cell 4: FS(4) = 1 TE(4) = 1 g(4) = 0
Cell 5: FS(5) = 1 TE(5) = 0 g(5) = 1
1
3
4
2
5
a
b
c
d
e
1
3
4
2
5
a
b
c
d
e

## Slide 38: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Maximum positive gain Gm of a pass
The maximum positive gain Gm is the cumulative cell gain of m moves that produce a minimum cut cost.
Gm is determined by the maximum sum of cell gains g over a prefix of m moves in a pass

## Slide 39: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Ratio factor
The ratio factor is the relative balance between the two partitions with respect to cell area.
It is used to prevent all cells from clustering into one partition.
The ratio factor r is defined as
where area(A) and area(B) are the total respective areas of partitions A and B

## Slide 40: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Balance criterion
The balance criterion enforces the ratio factor.
To ensure feasibility, the maximum cell area areamax(V) must be taken into account.
A partitioning of V into two partitions A and B is said to be balanced if
[ r ∙ area(V) – areamax(V) ] ≤ area(A) ≤ [ r ∙ area(V) + areamax(V) ]

## Slide 41: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Terminology
Base cell
A base cell is a cell c that has maximum cell gain g(c) among all free cells, and whose move does not violate the balance criterion.
Cell 1: FS(1) = 2 TE(1) = 1 g(1) = 1
Cell 2: FS(2) = 0 TE(2) = 1 g(2) = -1
Cell 3: FS(3) = 1 TE(3) = 1 g(3) = 0
Cell 4: FS(4) = 1 TE(4) = 1 g(4) = 0
Base cell

## Slide 42: Fiduccia-Mattheyses (FM) Algorithm – Terminology
Pin distribution of a net: The pair (A(net), B(net))
  where A(net): # of pins in partition A
  B(net): # of pins in partition B
Critical net: A net that contains a cell c whose move changes the cut state of the net
  Either: The net has 1 cell in partition A and all others in B
  Or: The net has all cells in a single partition
  For a critical cell, one of the following should hold:
    A(net) = 0 or A(net) = 1 or B(net) = 0 or B(net) = 1

## Slide 43: Fiduccia-Mattheyses (FM) Algorithm – Critical Nets
Critical nets simplify the gain calculations
  Only the cells belonging to critical nets need to be considered for gain calculations

## Slide 44: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm

## Slide 45: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Step 0: Compute the balance criterion
[ r ∙ area(V) – areamax(V) ] ≤ area(A) ≤ [ r ∙ area(V) + areamax(V) ]
0,375 * 16 – 5 = 1  area(A)  11 = 0,375 * 16 +5.
Given: Ratio factor r = 0,375
area(Cell_1) = 2 area(Cell_2) = 4 area(Cell_3) = 1 area(Cell_4) = 4 area(Cell_5) = 5.

## Slide 46: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Step 1: Compute the gains of each cell
Cell 1: FS(Cell_1) = 2 TE(Cell_1) = 1 g(Cell_1) = 1
Cell 2: FS(Cell_2) = 0 TE(Cell_2) = 1 g(Cell_2) = -1
Cell 3: FS(Cell_3) = 1 TE(Cell_3) = 1 g(Cell_3) = 0
Cell 4: FS(Cell_4) = 1 TE(Cell_4) = 1 g(Cell_4) = 0
Cell 5: FS(Cell_5) = 1 TE(Cell_5) = 0 g(Cell_5) = 1

## Slide 47: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Cell1: FS(Cell_1) = 2 TE(Cell_1) = 1 g(Cell_1) = 1
Cell 2: FS(Cell_2) = 0 TE(Cell_2) = 1 g(Cell_2) = -1
Cell 3: FS(Cell_3) = 1 TE(Cell_3) = 1 g(Cell_3) = 0
Cell 4: FS(Cell_4) = 1 TE(Cell_4) = 1 g(Cell_4) = 0
Cell 5: FS(Cell_5) = 1 TE(Cell_5) = 0 g(Cell_5) = 1
Step 2: Select the base cell
Possible base cells are Cell 1 and Cell 5
Balance criterion after moving Cell 1: area(A) = area(Cell_2) = 4
Balance criterion after moving Cell 5: area(A) = area(Cell_1) + area(Cell_2) + area(Cell_5) = 11
Both moves respect the balance criterion, but Cell 1 is selected, moved,
and fixed as a result of the tie-breaking criterion.

## Slide 48: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Step 3: Fix base cell, update g values
Cell 2: FS(Cell_2) = 2 TE(Cell_2) = 0 g(Cell_2) = 2
Cell 3: FS(Cell_3) = 0 TE(Cell_3) = 1 g(Cell_3) = -1
Cell 4: FS(Cell_4) = 0 TE(Cell_4) = 2 g(Cell_4) = -2
Cell 5: FS(Cell_5) = 0 TE(Cell_5) = 1 g(Cell_5) = -1
After Iteration i = 1: Partition A1 = 2, Partition B1 = 1,3,4,5, with fixed cell 1.

## Slide 49: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
1
3
4
2
5
A
B
a
b
c
d
e
Cell 2: FS(Cell_2) = 2 TE(Cell_2) = 0 g(Cell_2) = 2
Cell 3: FS(Cell_3) = 0 TE(Cell_3) = 1 g(Cell_3) = -1
Cell 4: FS(Cell_4) = 0 TE(Cell_4) = 2 g(Cell_4) = -2
Cell 5: FS(Cell_5) = 0 TE(Cell_5) = 1 g(Cell_5) = -1
Iteration i = 2
Cell 2 has maximum gain g2 = 2, area(A) = 0, balance criterion is violated.
Cell 3 has next maximum gain g2 = -1, area(A) = 5, balance criterion is met.
Cell 5 has next maximum gain g2= -1, area(A) = 9, balance criterion is met.
Move cell 3, updated partitions: A2 = {2,3}, B2 = {1,4,5}, with fixed cells {1,3}
Iteration i = 1

## Slide 50: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
Cell 2: g(Cell_2) = 1
Cell 4: g(Cell_4) = 0
Cell 5: g(Cell_5) = -1
Iteration i = 3
Cell 2 has maximum gain g3 = 1, area(A) = 1, balance criterion is met. Move cell 2, updated partitions: A3 = {3}, B3 = {1,2,4,5}, with fixed cells {1,2,3}
1
3
4
2
5
A
B
a
b
c
d
e
Iteration i = 2

## Slide 51: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
Cell 4: g(Cell_4) = 0
Cell 5: g(Cell_5) = -1
Iteration i = 4
Cell 4 has maximum gain g4 = 0, area(A) = 5, balance criterion is met. Move cell 4, updated partitions: A4 = {3,4}, B3 = {1,2,5}, with fixed cells {1,2,3,4}
1
3
4
2
5
B
A
a
b
c
d
e
Iteration i = 3

## Slide 52: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
Cell 5: g(Cell_5) = -1
Iteration i = 5
Cell 5 has maximum gain g5 = -1, area(A) = 10, balance criterion is met. Move cell 5, updated partitions: A4 = {3,4,5}, B3 = {1,2}, all cells {1,2,3,4,5} fixed.
1
3
4
2
5
B
A
a
b
c
d
e
Iteration i = 4

## Slide 53: 2.4.3 Fiduccia-Mattheyses (FM) Algorithm – Example
Step 5: Find best move sequence c1 … cm
G1 = g1 = 1 G2 = g1 + g2 = 0 G3 = g1 + g2 + g3 = 1 G4 = g1 + g2 + g3 + g4 = 1 G5 = g1 + g2 + g3 + g4 + g5 = 0.
Maximum positive cumulative gain
found in iterations 1, 3 and 4.
The move prefix m = 4 is selected due to the better balance ratio (area(A) = 5); the four cells 1, 2, 3 and 4 are then moved.
Result of Pass 1: Current partitions: A = {3,4}, B = {1,2,5}, cut cost reduced from 3 to 2.
1
3
4
2
5
B
A
a
b
c
d
e

## Slide 54: Chapter 2 Supplemental: Difference between KL & FM
Component dependency of partitioning algorithms
  KL is based on the number of edges
  FM is based on the number of nets
Time complexity of partitioning algorithms
  KL has cubic time complexity
  FM has linear time complexity
54

## Slide 55: Chapter 2 – Netlist and System Partitioning
2.1 Introduction
2.2 Terminology
2.3 Optimization Goals
2.4 Partitioning Algorithms
  2.4.1 Kernighan-Lin (KL) Algorithm
  2.4.2 Extensions of the Kernighan-Lin Algorithm
  2.4.3 Fiduccia-Mattheyses (FM) Algorithm
2.5 Framework for Multilevel Partitioning
  2.5.1 Clustering
  2.5.2 Multilevel Partitioning
2.6 System Partitioning onto Multiple FPGAs

## Slide 56: 2.5.1 Clustering
56
To make things easy, groups of tightly-connected nodes can be clustered, absorbing connections between these nodes
Size of each cluster is often limited so as to prevent degenerate clustering, i.e. a single large cluster dominates other clusters
Refinement should satisfy balance criteria

## Slide 57: 2.5.1 Clustering
a
b
c
d
e
a,b,c
d
e
a
b
d
c,e
Initital graph
Possible clustering hierarchies of the graph
© 2011 Springer

## Slide 58: 2.5.2 Multilevel Partitioning
© 2011 Springer Verlag

## Slide 59: FPGA Applications: Programmability
Instead of fabricating a chip, we can program an FPGA
Advantages:
  Avoid non-recurring engineering (NRE) costs of IC design
  Enable later changes easily (e.g. in case of a new media format)
Disadvantages:
  Larger area, more power, slower speed

## Slide 60: FPGA Applications: System Prototyping
Reduce time to market with system prototyping:
Typical design cycle:
Hardware design
Software design
Arch
RTL
PD
Litho
Fab
Firmware
Drivers
Apps
Arch
RTL
PD
Litho
Fab
Firmware
Drivers
Apps

## Slide 61: 2.6 System Partitioning onto Multiple FPGAs
FPGA
FPGA
FPGA
FPGA
FPIC
FPIC
FPIC
FPIC
FPGA
FPGA
RAM
Logic
Logic
Reconfigurable system with multiple FPGA and FPIC devices
Mapping of a typical system architecture onto multiple FPGAs
© 2011 Springer Verlag

## Slide 62: System Partitioning onto Multiple FPGAs
Challenges:
  Low utilization of FPGA resources (due to hard I/O pin limits)
  Low performance (due to interconnect delays between FPGAs)
  Long runtimes of system partitioning process
Partitioning formulations:
  Hard upper bound for total area of each partition
  Hard upper bound for the cut size
3rd dimension for FPGA mapping: time

## Slide 63: Summary of Chapter 2
Circuit netlists can be represented by graphs or hypergraphs
Partitioning a graph means assigning nodes to disjoint partitions
  Total size of each partition (number/area of nodes) is limited
  Objective: minimize the number connections between partitions
Basic partitioning algorithms
  Incremental changes organized into passes
  KL swaps pairs of nodes from different partitions
  FM re-assigns one node at a time
  FM is faster, usually more successful
Multilevel partitioning
  Clustering
  FM partitioning
  Refinement (also uses FM partitioning)
Application: system partitioning into FPGAs
  Each FPGA is represented by a partition