## Slide 1: Routing Topology Algorithms
Mustafa Ozdal

## Slide 2: Introduction
How to connect nets with multiple terminals?
Net topologies needed before point-to-point routing between terminals.
Several objectives:
  Minimum wirelength
  Best timing
  Routability

## Slide 3: Example
: receiver
: driver

## Slide 4: Example – Star topology (suboptimal)
: receiver
: driver
Connect each receiver to the driver independently.

## Slide 5: Example – Min Wirelength Topology
: receiver
: driver

## Slide 6: Outline
Definitions and basic algorithms
  Minimum Spanning Trees (MST)
  Steiner Trees
  Rectilinear Steiner Trees
Wirelength vs timing tradeoff

## Slide 7: Minimum Spanning Tree (MST)
Consider a connected graph G = (V, E)
  V: terminals
  E: potential connections between terminals
  w(e): wirelength of edge e
MST: The set of edges ET such that:
  ET is a subset of E
  The graph T = (V, ET) is connected
  The total edge weight of ET is minimum

## Slide 8: MST Example
5 vertices
10 edges
Weight of edge e is the Manhattan distance of e
What is the MST?

## Slide 9: MST Example
The edge set ET:
  W(ET) is minimum
  T = (V, ET) is still connected
Note: T = (V, ET) must contain n vertices and n-1 edges.

## Slide 10: Kruskal’s MST Algorithm
Initialize T as empty set
Define a disjoint set corresponding to each vertex in V.
Sort edges in non-decreasing order of weights
For each e = (v1, v2) in the sorted edge list
  If v1 and v2 belong to different sets
    Add e to T
    Merge the sets corresponding to v1 and v2
Return T

## Slide 11: Kruskal’s MST Algorithm - Example
Initially, each vertex is a disjoint set (different color)
We will process edges from shortest to longest

## Slide 12: Kruskal’s MST Algorithm – Example Step 1
Start from the shortest edge
The vertices connected are in different sets
Add the edge to MST
Merge the vertices

## Slide 13: Kruskal’s MST Algorithm - Example Step 2
Process the next shortest edge.
The vertices connected are in different sets
Add the edge to MST
Merge the vertices

## Slide 14: Kruskal’s MST Algorithm – Example Step 3
Process the next shortest edge.
The vertices connected are in different sets
Add the edge to MST
Merge the vertices

## Slide 15: Kruskal’s MST Algorithm – Example Step 4
Process the next shortest edge.
The vertices connected are in different sets
Add the edge to MST
Merge the vertices

## Slide 16: Kruskal’s MST Algorithm – Example Step 5
Process the next shortest edge.
The vertices connected are in the same set
Skip the edge

## Slide 17: Kruskal’s MST Algorithm – Example Step 6
Process the next shortest edge.
The vertices connected are in different sets
Add the edge to MST
Merge the vertices

## Slide 18: Kruskal’s MST Algorithm – Example Step 7
All vertices are connected
MST edges are highlighted

## Slide 19: Prim’s MST Algorithm
Initialize VT and MST to be empty set
Pick a root vertex v in V (e.g. driver terminal)
Add v to VT
While VT is not equal to V
  Find edge e = (v1, v2) such that
    v1 is in VT
    v2 is NOT in VT
    weight of e is minimum
  Add e to MST
  Add v2 to VT
Return MST

## Slide 20: Prim’s MST Algorithm - Example
Initially, VT contains the root vertex (e.g. driver)

## Slide 21: Prim’s MST Algorithm - Example
Pick the shortest edge between VT and V - VT
Add that edge to MST
Expand VT

## Slide 22: Prim’s MST Algorithm - Example
Pick the shortest edge between VT and V - VT
Add that edge to MST
Expand VT

## Slide 23: Prim’s MST Algorithm - Example
Pick the shortest edge between VT and V - VT
Add that edge to MST
Expand VT

## Slide 24: Prim’s MST Algorithm - Example
Pick the shortest edge between VT and V - VT
Add that edge to MST
Expand VT

## Slide 25: Prim’s MST Algorithm - Example
Pick the shortest edge between VT and V - VT
Add that edge to MST
Expand VT

## Slide 26: Prim’s MST Algorithm - Example
Pick the shortest edge between VT and V - VT
Add that edge to MST
Expand VT

## Slide 27: Prim’s MST Algorithm - Example
All vertices are included in VT
MST edges are highlighted

## Slide 28: MST – Summary
Find the min-cost edge set that connects a given vertex set.
Possible to solve it optimally in O(ElogE) time
  Kruskal’s algorithm
  Prim’s algorithm
In general Prim’s algorithm is better to control timing tradeoffs because we expand a wavefront from the driver.

## Slide 29: Steiner Trees
Similar to MSTs, but:
  Extra intermediate vertices can be added to reduce wirelength.
MST
Steiner tree
Steiner point

## Slide 30: Rectilinear Steiner Trees
Steiner trees of which edges are all Manhattan
  i.e. The routing of the slanted edges are all pre-determined
Steiner tree
Rectilinear Steiner tree

## Slide 31: Steiner Tree Algorithms
Steiner tree problem is NP-complete
  Most likely there’s no polynomial time optimal algorithm
  Note: MST problem can be solved optimally in O(ElogE)
Many Steiner tree heuristics
  Iteratively add Steiner points to an MST
  Route each edge of MST allowing Steiner points be created in the process.
  Exponential time algorithms: Based on ILP, SAT, SMT solvers
  A popular and practical algorithm: FLUTE
    C. Chu et al., “FLUTE: Fast Lookup Table Based Rectilinear Steiner Minimal Tree Algorithm for VLSI Design”, IEEE Trans. On CAD, Jan 2008.

## Slide 32: FLUTE for Steiner Tree Generation Example
“Press” terminals from each side

## Slide 33: FLUTE for Steiner Tree Generation Example
Press from left
From the leftmost terminal to the second leftmost one.

## Slide 34: FLUTE for Steiner Tree Generation Example
Create a Steiner edge corresponding to pressing edge
Create a Steiner point at the new location
Steiner point
It is proven that pressing maintains optimality of Steiner tree.

## Slide 35: FLUTE for Steiner Tree Generation Example
Press from top

## Slide 36: FLUTE for Steiner Tree Generation Example
Press from top

## Slide 37: FLUTE for Steiner Tree Generation Example
Press from right

## Slide 38: FLUTE for Steiner Tree Generation Example
Press from bottom

## Slide 39: FLUTE for Steiner Tree Generation Example
Problem is reduced to the rectangle at the center.
How to connect these 4 Steiner (orange) points?

## Slide 40: FLUTE for Steiner Tree Generation Example
FLUTE pre-computes all Steiner tree solutions for such rectangles up to 10 terminals.
After pressing, if there are less than 10 nodes, returns the solution from database.

## Slide 41: FLUTE for Steiner Tree Generation
The solutions for simple problems are stored in a database.
After pressing operations, if the problem is turned into one of those in the database, the best solution in the database is returned.
If not in the database, use reduction heuristics.
Canonical solutions stored in database

## Slide 42: FLUTE for Steiner Tree Generation Example
Solution inside the center rectangle is chosen from the database.

## Slide 43: FLUTE for Steiner Tree Generation Example
Final rectilinear Steiner tree

## Slide 44: Cost Metrics
Many tradeoffs to consider for routing topologies
Topology with best wirelength can have poor timing
Topology with best wirelength and timing may not be routable

## Slide 45: Example Wirelength/Timing Tradeoff
: receiver
: driver

## Slide 46: Example Min Wirelength
: receiver
: driver

## Slide 47: Example Min Wirelength
: receiver
: driver
Large delay
to receiver

## Slide 48: Example Better Timing – Worse Wirelength
: receiver
: driver