## Slide 1: Edge Detection
Selim Aksoy
Department of Computer Engineering
Bilkent University
saksoy@cs.bilkent.edu.tr

## Slide 2: Edge detection
Edge detection is the process of finding meaningful transitions in an image.
The points where sharp changes in the brightness occur typically form the border between different objects or scene parts.
Further processing of edges into lines, curves and circular arcs result in useful features for matching and recognition.
Initial stages of mammalian vision systems also involve detection of edges and local features.

## Slide 3: Edge detection
Sharp changes in the image brightness occur at:
  Object boundaries
    A light object may lie on a dark background or a dark object may lie on a light background.
  Reflectance changes
    May have quite different characteristics – zebras have stripes, and leopards have spots.
  Cast shadows
  Sharp changes in surface orientation

## Slide 4: Edge models

## Slide 5: Difference operators for 2D

## Slide 6: Difference operators for 2D

## Slide 7: Difference operators for 2D
Adapted from Gonzales and Woods

## Slide 8: Difference operators for 2D

## Slide 9: Difference operators under noise
Solution is to smooth first:
Adapted from Steve Seitz

## Slide 10: Difference operators under noise
Differentiation property of convolution:
Adapted from Steve Seitz

## Slide 11: Difference operators under noise
Consider:
Adapted from Steve Seitz
Laplacian of Gaussian
operator

## Slide 12: Edge detection filters for 2D
Laplacian of Gaussian
Gaussian
derivative of Gaussian
Adapted from Steve Seitz, U of Washington

## Slide 13: Difference operators for 2D

## Slide 14: Difference operators for 2D

## Slide 15: Edge detection
Three fundamental steps in edge detection:
  Image smoothing: to reduce the effects of noise.
  Detection of edge points: to find all image points that are potential candidates to become edge points.
  Edge localization: to select from the candidate edge points only the points that are true members of an edge.

## Slide 16: Canny edge detector
Smooth the image with a Gaussian filter with spread σ.
Compute gradient magnitude and direction at each pixel of the smoothed image.
Zero out any pixel response less than or equal to the two neighboring pixels on either side of it, along the direction of the gradient (non-maxima suppression).
Track high-magnitude contours using thresholding (hysteresis thresholding).
Keep only pixels along these contours, so weak little segments go away.

## Slide 17: Canny edge detector
Original image (Lena)
Adapted from Steve Seitz, U of Washington

## Slide 18: Canny edge detector
Adapted from Steve Seitz, U of Washington
Magnitude of the gradient

## Slide 19: Canny edge detector
Adapted from Steve Seitz, U of Washington
Thresholding

## Slide 20: Canny edge detector
Adapted from Steve Seitz, U of Washington
How to turn these thick regions of the gradient into curves?

## Slide 21: Canny edge detector
Non-maxima suppression:
  Check if pixel is local maximum along gradient direction.
  Select single max across width of the edge.
  Requires checking interpolated pixels p and r.
  This operation can be used with any edge operator when thin boundaries are wanted.

## Slide 22: Canny edge detector
Adapted from Steve Seitz, U of Washington
Problem: pixels along this edge did not survive the thresholding

## Slide 23: Canny edge detector
Hysteresis thresholding:
  Use a high threshold to start edge curves, and a low threshold to continue them.

## Slide 24: Canny edge detector

## Slide 25: Canny edge detector

## Slide 26: Canny edge detector
The Canny operator gives single-pixel-wide images with good continuation between adjacent pixels.
It is the most widely used edge operator today; no one has done better since it came out in the late 80s. Many implementations are available.
It is very sensitive to its parameters, which need to be adjusted for different application domains.

## Slide 27: Edge linking
Hough transform
  Finding line segments
  Finding circles
Model fitting
  Fitting line segments
  Fitting ellipses
Edge tracking

## Slide 28: Fitting: main idea
Choose a parametric model to represent a set of features
Membership criterion is not local
  Cannot tell whether a point belongs to a given model just by looking at that point
Three main questions:
  What model represents this set of features best?
  Which of several model instances gets which feature?
  How many model instances are there?
Computational complexity is important
  It is infeasible to examine every possible set of parameters and every possible combination of features
Adapted from Kristen Grauman

## Slide 29: Example: line fitting
Why fit lines?
  Many objects characterized by presence of straight lines
Adapted from Kristen Grauman

## Slide 30: Difficulty of line fitting
Extra edge points (clutter), multiple models:
  which points go with which line, if any?
Only some parts of each line detected, and some parts are missing:
  how to find a line that bridges missing evidence?
Noise in measured edge points, orientations:
  how to detect true underlying parameters?
Adapted from Kristen Grauman

## Slide 31: Voting
It is not feasible to check all combinations of features by fitting a model to each possible subset.
Voting is a general technique where we let each feature vote for all models that are compatible with it.
  Cycle through features, cast votes for model parameters.
  Look for model parameters that receive a lot of votes.
Noise and clutter features will cast votes too, but typically their votes should be inconsistent with the majority of “good” features.
Adapted from Kristen Grauman

## Slide 32: Hough transform
The Hough transform is a method for detecting lines or curves specified by a parametric function.
If the parameters are p1, p2, … pn, then the Hough procedure uses an n-dimensional accumulator array in which it accumulates votes for the correct parameters of the lines or curves found on the image.
y = mx + b
image
m
b
accumulator
Adapted from Linda Shapiro, U of Washington

## Slide 33: Hough transform: line segments
Adapted from Steve Seitz, U of Washington
Connection between image (x,y) and Hough (m,b) spaces
  A line in the image corresponds to a point in Hough space
  To go from image space to Hough space:
    given a set of points (x,y), find all (m,b) such that y = mx + b
  What does a point (x0, y0) in the image space map to?
    Answer: the solutions of b = -x0m + y0
    This is a line in Hough space
x
y
m
b
Image space
Hough (parameter) space
x0
y0

## Slide 34: Hough transform: line segments
What are the line parameters for the line that contains both (x0, y0) and (x1, y1)?
  It is the intersection of the lines b = –x0m + y0 and b = –x1m + y1
x
y
m
b
Image space
Hough (parameter) space
x0
y0
b = –x1m + y1
(x0, y0)
(x1, y1)
Adapted from Steve Seitz, U of Washington

## Slide 35: Hough transform: line segments
y = mx + b is not suitable (why?)
The equation generally used is:
d = r sin(θ) + c cos(θ).
d

r
c
d is the distance from the line to origin.
θ is the angle the perpendicular makes
with the column axis.
Adapted from Linda Shapiro, U of Washington

## Slide 36: Hough transform: line segments
Adapted from Shapiro and Stockman

## Slide 37: Hough transform: line segments

## Slide 38: Hough transform: line segments

## Slide 39: Hough transform: line segments

## Slide 40: Hough transform: circles
Main idea: The gradient vector at an edge pixel points the center of the circle.
Circle equations:
  r = r0 + d sin(θ) r0, c0, d are parameters
  c = c0 + d cos(θ)
*(r,c)
d
Adapted from Linda Shapiro, U of Washington

## Slide 41: Hough transform: circles
Adapted from Shapiro and Stockman

## Slide 42: Hough transform: circles
http://docs.opencv.org/2.4/doc/tutorials/imgproc/imgtrans/hough_circle/hough_circle.html
https://www.mathworks.com/help/images/ref/imfindcircles.html
http://shreshai.blogspot.com.tr/2015/01/matlab-tutorial-finding-center-pivot.html

## Slide 43: Hough transform: circles
Zhao et al., “Oil Tanks Extraction from High Resolution Imagery Using a Directional and Weighted Hough Voting Method”, Journal of the Indian Society of Remote Sensing, September 2015

## Slide 44: Model fitting
Mathematical models that fit data not only reveal important structure in the data, but also can provide efficient representations for further analysis.
Mathematical models exist for lines, circles, cylinders, and many other shapes.
We can use the method of least squares for determining the parameters of the best mathematical model fitting the observed data.

## Slide 45: Model fitting: line segments
Adapted from Martial Hebert, CMU

## Slide 46: Model fitting: line segments

## Slide 47: Model fitting: line segments

## Slide 48: Model fitting: line segments
Problems in fitting:
  Outliers
  Error definition (algebraic vs. geometric distance)
  Statistical interpretation of the error (hypothesis testing)
  Nonlinear optimization
  High dimensionality (of the data and/or the number of model parameters)
  Additional fit constraints

## Slide 49: Model fitting: ellipses

## Slide 50: Model fitting: ellipses
Adapted from Andrew Fitzgibbon, PAMI 1999

## Slide 51: Model fitting: ellipses
Adapted from Andrew Fitzgibbon, PAMI 1999

## Slide 52: Edge tracking
Mask-based approach uses masks to identify the following events:
  start of a new segment,
  interior point continuing a segment,
  end of a segment,
  junction between multiple segments,
  corner that breaks a segment into two.
junction
corner
Adapted from Linda Shapiro, U of Washington

## Slide 53: Example: object extraction
by Serkan Kiranyaz Tampere University of Technology

## Slide 54: Example: object extraction

## Slide 55: Example: object extraction

## Slide 56: Example: object recognition
Mauro Costa’s dissertation at the University of Washington for recognizing 3D objects having planar, cylindrical, and threaded surfaces:
  Detects edges from two intensity images.
  From the edge image, finds a set of high-level features and their relationships.
  Hypothesizes a 3D model using relational indexing.
  Estimates the pose of the object using point pairs, line segment pairs, and ellipse/circle pairs.
  Verifies the model after projecting to 2D.

## Slide 57: Example: object recognition
Example scenes used. The labels “left” and “right” indicate the direction of the light source.

## Slide 59: Example: object recognition

## Slide 60: Example: object recognition
1 coaxials-
multi
3 parallel
lines
2 ellipse
encloses
encloses
encloses
coaxial
1 1 2 3
2 3 3 2
e e e c
Relationship graph and the corresponding 2-graphs.

## Slide 61: Example: object recognition
Learning phase: relational indexing by encoding each 2-graph and storing in a hash table.
Matching phase: voting by each 2-graph observed in the image.

## Slide 62: Example: object recognition
The matched features of the hypothesized object are used to determine its pose.
The 3D mesh of the object is used to project all its features onto the image.
A verification procedure checks how well the object features line up with edges on the image.
Incorrect hypothesis