## Slide 1: Digital Image Fundamentals
Selim Aksoy
Department of Computer Engineering
Bilkent University
saksoy@cs.bilkent.edu.tr

## Slide 2: Imaging process
Light reaches surfaces in 3D.
Surfaces reflect.
Sensor element receives light energy.
Intensity is important.
Angles are important.
Material is important.
Adapted from Rick Szeliski

## Slide 3: Physical parameters
Geometric
  Type of projection
  Camera pose
Optical
  Sensor’s lens type
  Focal length, field of view, aperture
Photometric
  Type, direction, intensity of light reaching sensor
  Surfaces’ reflectance properties
Sensor
  Sampling, etc.
Adapted from Trevor Darrell, UC Berkeley

## Slide 4: Image acquisition
Adapted from Rick Szeliski

## Slide 5: Camera calibration
Camera’s extrinsic and intrinsic parameters are needed to calibrate the geometry.
Extrinsic: camera frame  world frame
Intrinsic: image coordinates relative to camera  pixel coordinates
Camera frame
World frame
Adapted from Trevor Darrell, UC Berkeley

## Slide 6: Eyes: projection onto retina
Adapted from Joseph Redmon, U of Washington

## Slide 7: Model: pinhole camera
Adapted from Joseph Redmon, U of Washington

## Slide 8: Model: pinhole camera
Adapted from Joseph Redmon, U of Washington

## Slide 9: Image: 3d->2d projection of the world
Adapted from Joseph Redmon, U of Washington

## Slide 10: Image: 3d->2d projection of the world
Adapted from Joseph Redmon, U of Washington

## Slide 11: Image: 3d->2d projection of the world
Adapted from Joseph Redmon, U of Washington

## Slide 12: Image: 3d->2d projection of the world
Adapted from Joseph Redmon, U of Washington

## Slide 13: Image: 3d->2d projection of the world
Adapted from Joseph Redmon, U of Washington

## Slide 14: How do we record color?
Adapted from Joseph Redmon, U of Washington
At each point we record incident light

## Slide 15: How do we record color?
Adapted from Joseph Redmon, U of Washington
Bayer pattern for CMOS sensors

## Slide 16: Focal length
Field of view depends on focal length.
As f gets smaller, image becomes more wide angle
  more world points project onto the finite image plane
As f gets larger, image becomes more telescopic
  smaller part of the world projects onto the finite image plane
Adapted from Trevor Darrell, UC Berkeley

## Slide 17: Focal length
Adapted from Matthew Brown, U of Washington

## Slide 18: Aperture
A real camera must have a finite aperture to get enough light, but this causes blur in the image
Solution: use a lens to focus light onto the image plane
Adapted from Matthew Brown, U of Washington

## Slide 19: Aperture
Adapted from Matthew Brown, U of Washington
Note that lenses focus all rays from a plane in the world
Objects off the plane are blurred depending on distance

## Slide 20: Aperture
Adapted from Matthew Brown, U of Washington
Smaller aperture -> smaller blur, larger depth of field

## Slide 21: Shutter speed
Adapted from Matthew Brown, U of Washington

## Slide 22: Sampling and quantization

## Slide 23: Sampling and quantization

## Slide 24: Image representation
Images can be represented by 2D functions of the form f(x,y).
The physical meaning of the value of f at spatial coordinates (x,y) is determined by the source of the image.
Adapted from Shapiro and Stockman

## Slide 25: Image representation
In a digital image, both the coordinates and the image value become discrete quantities.
Images can now be represented as 2D arrays (matrices) of integer values: I[i,j] (or I[r,c]).
The term gray level is used to describe monochromatic intensity.

## Slide 26: Spatial resolution
Spatial resolution is the smallest discernible detail in an image.
Sampling is the principal factor determining spatial resolution.

## Slide 27: Gray level resolution
Gray level resolution refers to the smallest discernible change in gray level (often power of 2).

## Slide 28: Bit planes

## Slide 29: Electromagnetic (EM) spectrum

## Slide 30: Electromagnetic (EM) spectrum
The wavelength of an EM wave required to “see” an object must be of the same size as or smaller than the object.

## Slide 31: Other types of sensors

## Slide 32: Other types of sensors

## Slide 33: Other types of sensors
blue green red
near ir middle ir thermal ir middle ir

## Slide 34: Other types of sensors
©IEEE

## Slide 35: Other types of sensors

## Slide 36: Other types of sensors

## Slide 37: Other types of sensors

## Slide 38: Other types of sensors

## Slide 39: Image enhancement
The principal objective of enhancement is to process an image so that the result is more suitable than the original for a specific application.
Enhancement can be done in
  Spatial domain,
  Frequency domain.
Common reasons for enhancement include
  Improving visual quality,
  Improving machine recognition accuracy.

## Slide 40: Image enhancement
Transformation function of the form s = T(r) where “r” is the original pixel value and “s” is the new value after enhancement.

## Slide 41: Image enhancement

## Slide 42: Image enhancement

## Slide 43: Image enhancement

## Slide 44: Image enhancement
Contrast stretching:

## Slide 45: Histogram processing

## Slide 46: Histogram processing
Intuitively, we expect that an image whose pixels
  tend to occupy the entire range of possible gray levels,
  tend to be distributed uniformly
will have a high contrast and show a great deal of gray level detail.
It is possible to develop a transformation function that can achieve this effect using histograms.

## Slide 47: Histogram equalization
http://fourier.eng.hmc.edu/e161/lectures/contrast_transform/node3.html

## Slide 48: Histogram equalization
Adapted from Wikipedia

## Slide 49: Enhancement using arithmetic operations

## Slide 50: Enhancement using color channels
Adapted from Joseph Redmon, U of Washington
RGB
Hue
Saturation
Value

## Slide 51: Enhancement using color channels
Adapted from Joseph Redmon, U of Washington
More saturation -> intense colors
2x

## Slide 52: Enhancement using color channels
Adapted from Joseph Redmon, U of Washington
More value -> lighter image
2x

## Slide 53: Enhancement using color channels
Adapted from Joseph Redmon, U of Washington
Shift hue -> shift colors
-.2

## Slide 54: Enhancement using color channels
Adapted from Joseph Redmon, U of Washington
Set hue to your favorite color

## Slide 55: Enhancement using color channels
Adapted from Joseph Redmon, U of Washington
… or patterns

## Slide 56: Enhancement using color channels
Adapted from Joseph Redmon, U of Washington
Increase and threshold saturation

## Slide 57: Image formats
Popular formats:
  BMP Microsoft Windows bitmap image
  EPS Adobe Encapsulated PostScript
  GIF CompuServe graphics interchange format
  JPEG Joint Photographic Experts Group
  PBM Portable bitmap format (black and white)
  PGM Portable graymap format (gray scale)
  PPM Portable pixmap format (color)
  PNG Portable Network Graphics
  PS Adobe PostScript
  TIFF Tagged Image File Format

## Slide 58: Image formats
ASCII or binary
Number of bits per pixel (color depth)
Number of bands
Support for compression (lossless, lossy)
Support for metadata
Support for transparency
Format conversion
…
http://en.wikipedia.org/wiki/Comparison_of_graphics_file_formats