## Slide 1: Skuller: A volumetric shape registration algorithm for modeling skull deformities
Yusuf Sahillioğlu1 and Ladislav Kavan2
Medical Image Analysis 2015
Computer Eng. Depts, 1, Turkey
2, USA.
Notes: Follow in slide show (F5) mode for the explanatory animations.

## Slide 2
Medical objective
  Quantify the deviation of given skull from a healthy one.
Geometric objective:
  Develop an algorithm for volumetric registration of 3D
  shapes.
Problem Statement

## Slide 3
Shape registration:
Statistical shape analysis:
Objective quantification
of medical condition(s):
Applications

## Slide 4
A fast and robust solution to a new version of the well-
known shape registration problem, namely the registration
of two volumetric shapes.
  Source: volumetric tetrahedral mesh.
  Target: volumetric shape defined by voxels.
In contrast to point- and surface-based registration
techniques, our method better captures volumetric nature
of the data, such as bone thickness.
ICP with adaptive scaling.
Multi-initialization ICP.
Contributions

## Slide 5
Input: A tetrahedral mesh & A voxelized object (CT scan).
Input pair differs by non-isometric/non-rigid transformation.
//an isometric pair
Scope

## Slide 6
Overview.
Algorithm

## Slide 7
Initial alignment.
A global rigid alignment.
  Rotation, translation, uniform scale.
Treat input pair as 3D point clouds.
PCA-based alignment for
multiple ICP initialization.
Algorithm

## Slide 8
Initial alignment.
A global rigid alignment.
  Rotation, translation, uniform scale.
Treat input pair as 3D point clouds.
Solve for uniform scale u in addition
to the translation d once you have the
ICP-rotated points p.
Algorithm

## Slide 9
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Seek t that minimizes the following energy:
Algorithm

## Slide 10
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Correspondence/matching term.
  Brings transformed vertices t to the scan voxels s as close as
  possible.
  Permutation matrix P defines closest-point correspondences.
Algorithm

## Slide 11
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Regularization term: Volumetric Dirichlet energy.
  Preserves rest-pose coordinates t0, hence the good shape, as much
  as possible.
Algorithm

## Slide 12
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Regularization term: Volumetric Dirichlet energy.
  Measures deviation of tetrahedra’s deformation gradients F from I using the mesh Laplacian L.
Algorithm

## Slide 13
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Regularization term: Volumetric Dirichlet energy.
  Measures deviation of tetrahedra’s deformation gradients F from I using the mesh Laplacian L.
    , where Gj extracts vectorized gradient Fj
    when multiplied with all vertices, i.e.,
Algorithm

## Slide 14
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Regularization term: Tiknohonov energy.
  Keeps the amount of displacement from the previous step’s coordinates tprev as small as possible, i.e., no jumps.
Algorithm

## Slide 15
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Differentiating overall energy w.r.t. t gives:
Setting this derivative to 0 gives a sparse linear sys to solve:
Algorithm

## Slide 16
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Tricks to make this process work well.
  Adaptive weighting.
  Initially high \alpha \beta as the closest-point correspondences in P
  are not so reliable.
    Regularization (\alpha \beta) prevents a potential damage from Ecorr.
  Reduce regularization strength when t is very close to tprev, i.e., little/no progress.
    Ecorr becomes more reliable thanks to better correspondences.
Algorithm

## Slide 17
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Tricks to make this process work well.
  Adaptive weighting.
  Little displacement b/w iter 4 & 5 triggers adaptive weighting.
Algorithm

## Slide 18
Volumetric registration.
A non-rigid alignment.
  Bending/warping allowed.
Tricks to make this process work well.
  Ecorr disabling.
  A vertex that is already inside the volume should not be affected
  by Ecorr as it is not possible to establish meaningful matches now.
  Instead it should be free to move as dictated by regularization.
Algorithm

## Slide 19
Computational complexity.
n tetrahedral mesh vertices, m scan voxels.
Initial global alignment.
  O(nlogm) due to closest-point search.
Volumetric registrations.
    O(nlogm) due to closest-point search.
    O(n + w) Cholesky factorization performed i times, where i = #
    deformation iterations is about 20 in our runs. w high constant.
Algorithm

## Slide 20
Computational complexity.
n tetrahedral mesh vertices, m scan voxels.
Initial global alignment.
  O(nlogm) due to closest-point search.
Volumetric registrations.
    O(nlogm) due to closest-point search.
    O(n + w) Cholesky factorization performed i times, where i = #
    deformation iterations is about 20 in our runs. w high constant.
Execution time on a 2.2 GHz PC.
  Input tetrahedral mesh: 160K vertices, 560K tetrahedra.
  Input CT scan: 190K voxels.
  20 minutes.
    133 secs initial alignment, 1 sec (closest-point) + 49 sec (Cholesky) per
    deformation iteration.
Algorithm

## Slide 21
Results
//Initial global alignment.
//Resulting registered model.
//Underlying ground-truth surf.
//(extracted by Marching Cubes)
//Deformation process.

## Slide 22
Results
//Initial global alignment.
//Resulting registered model.

## Slide 23
Results
//Initial global alignment and //resulting registered model.
//Underlying ground-truth surf.

## Slide 24
Results
//Initial global alignment.
//Resulting registered model.
//Underlying ground-truth surf.

## Slide 25
Results
//Our volumetric registration //that respects bone thickness //(left column) is favorable over //unscreened and screened //Poisson surface registrations.

## Slide 26
Results
//Our volumetric registration //in comparison with volumetric //image registration techniques.

## Slide 27
Applications
//Transfer of colors (or any //other attributes) through the
//dense correspondence //achieved b/w the template and
//deformed/registered pose, and //effectively between ground- //truth geometries of all the //example skulls

## Slide 28
Applications
//Objective quantification of //severity of skull deformities. //Rig designed specifically for //the template mesh (top) //enables interactive //deformation of the registered //model using ARAP energy. //The effort of the doctor during //this session, i.e., the //deformation energy, is used as //the objective quantification //(bottom).

## Slide 29
Identify most efficient user interfaces for quantification.
Data-driven statistical models for quantification.
Remeshing algorithms to handle the missing data (teeth) or
the finest details (cracks) in the CT scans.
Future Work

## Slide 30
Fast and robust solution to volumetric registration of 3D
solid shapes.
Volumetric deformation energy plus additional tricks such as disabling of correspondence term and adaptive weighting.
Faster than registering volume images as mostly done in the medical imaging community.
  Also using a template mesh makes it robust to outliers.
More accurate than surface registration as mostly done in computer graphics community.
Side contributions for ICP (uniform scale, multi-init).
Cool apps.
  Dense correspondence and objective quantification.
Conclusion

## Slide 31
Asst. Prof. Yusuf Sahillioğlu, METU, Turkey.
Asst. Prof. Ladislav Kavan, UPenn, USA.
People